## Slide 1: LogAnalyzer Tool
Target group
Aim
Author
Department

## Slide 2: LogAnalyser Tool Introduction
Purpose:
Assist user in analyzing and debugging issue
  In helping users better understand the issue log and further analyze the operational data to know an overview of the system
Features:
Data parsing
  Dedicated for MeRiT CreateSupportInfo log
  Support formats of log files below (more types support is possible in the future)
    LogService.txt, Install.txt, mjnxtdebug.log, Protocol.txt, and ProcessLog.csv
Data Visualization
  Provide multiple chart generation options
    including load/unload time charts, duration charts, CTR, and protocol trend chart.
  Visualize open/close status of valves, aiding users in grasping the MSC status.
Data Export (Excel)
  For post-analysis and data storage

## Slide 3: GUI Layout Introduction
Display panel
Function tab
Tool layout introduction:
Menu bar
  File - log path select
  Log – log type select
  About – version information
Function tab
  Work flow
  Mask ID analysis
  Install log
  MSC info
Log path
  Selected file path
Display panel
  Parsed information
Status panel
  Information notice
Progress bar
  Parsing progress
Log path
Menu bar
Status panel
Progress status

## Slide 4: Log Parsing Operation
Select log (1)
Log path select (method 1):
Menu bar -> File -> Open Folder
The path name will be shown after selected
log path after selected

## Slide 5: Log Parsing Operation
Select log (2)
Log path select (method 2):
Tree view -> Navigate the file path
The path name will be shown after selected
log path after selected

## Slide 6: Log Parsing Operation
Select log type
File type select:
Menu bar -> Log -> choose the type below
  LogService
  Install
  mjnxtdebug
  Protocol
Current supported types

## Slide 7: Log Parsing Operation
Parse log file
Log file parse:
Press “Process” button
Through the status panel to check if the file parsing is successful or not
If parsing is completed, the window will pop out
If the error occurs, panel will show the error message and window pop out accordingly
Press “Process”

## Slide 8: Work Flow
Function introduction
Load/Unload information display area
WorkFlow Tab:
Load / Unload information area
  Loaded / Unloaded timestamp
  Load / Unload cost time
Workflow steps area
  Depending on the selected item of left area
  Display work steps for the specific mask ID
Work steps display area

## Slide 9: Mask ID Analysis
Function introduction
Mask ID Analysus Tab:
Load/Unload Time Chart button
  Show load/unload time information for the specific mask
Duration Time Chart button
  Show load/unload duration time for the specific mask

## Slide 10: Install Log
Function introduction
Install Log Tab:
Information panel
  Show SW installing history

## Slide 11: MSC Info
Function introduction
MSC Info Tab:
MSC protocol
  Select 2.x or 3.x MSC fw version
CTR/MFC filter
  Gauge display filter
Parsing file source
  Select the log source is mjnxtdebug.log or protocol.txt
Protocol information
  Information from parsed protocol.txt
MSC time filter
  Time filtered depends on the mjnxtdebug.log
MSC valve diaggram
  Show valve status
Generate chart button
  Generate the chart
Export button
  Export to Excel
MSC protocol
CTR/MFC filter
Parsing file source
Protocol information
MSC log time filter
MSC valve diagram
Trend chart
Generate chart
Export to Excel

## Slide 12: MSC Info
Valve information window
Valve state window:
Press Valve State button
  Valve state will be displayed based on the time slice
CTR/MFC filter